## Slide 1: Preliminary Design review
Samuel Ellison
Group 8

## Slide 2: Project overview
Section 1

## Slide 3: Theory: Thermistors
Thermistors
Resistor with resistance dependent on temperature
Two types
  NTC: resistance decreases with increasing temp (this case)
  PTC: resistance increases with increasing temp
Notes: I’ll start by discussing the theory of thermistors. A thermistor is simply a resistor with a resistance that changes with the ambient temperature. The type of thermistor determines how the resistance changes with temperature. The two types are Negative and Positive Temperature Coefficient Thermistors. The relationships are shown in the graph here: resistance decreases with an increase in temp for NTC, and increases with an increase in temp for PTC.

## Slide 4: Theory: NTC T-R Models
Steinhart-Hart Equation
Third order approximation, constants can be solved with three R-T data points:
Parameter Equation
Alternative form of S-H with
Requires only one R-T data point
usually very small, accurate proxy
value given in manufacturer specs
Notes: The type of thermistor I will be using is an NTC. There are mainly two models that are used to calculate temperature from an NTC thermistor: SH and beta parameter. The SH is a third order approximation and uses three coefficients unique to the thermistor. The beta parameter is an alternative and simpler form of SH that uses just one coefficient: the beta parameter. It’s assumed in this model that the last coefficient c2 in SH is about 0, which is the case most of the time. The SH coefficients and beta parameter are sometimes given in the manufacturer specs. However, I will be deriving my coefficients from a calibration of the thermistor using three measured temperatures and resistances, which I will discuss in detail later on. All temperatures must be in Kelvin when using these models.

## Slide 5: Theory: Voltage Dividers
Voltage Divider
  Circuit producing output voltage proportional to input
  Used to measure resistance of unknown resistor
Thermistor Resistance
  Voltage divider used to calculate thermistor resistance
Equation
If is the unknown thermistor resistance
measured by Arduino, V, is resistance of known resistor
Notes: Voltage Dividers are extremely useful circuit components, especially when working with Arduino. The circuit produces an output voltage proportional to the input voltage based on resistance values R1 and R2. The purpose of using a voltage divider in general is to measure the resistance of an unknown resistor (R2 in circuit). When applied to Arduino, voltage dividers are important because the digital and analog signals going to the microcontroller can only read voltage output, not resistance. So measuring the thermistor’s resistance requires the use of a voltage divider. GO THROUGH EQUATIONS. Voltage dividers in general do not have to use resistors, but in this project they do.

## Slide 6: Theory: Thermal Time Constant
Thermal time constant is time required for thermistor to reach 63.2% of difference between initial and final ambient temperatures
Assuming a lumped capacitance model for transient temperature analysis,
where and are the ambient temperatures and is the thermistor’s reading at time .
If , then

## Slide 7: Requirements
Objective: Design an electro-thermal system using Arduino kit with NTC thermistor
Thermometer measurement of freezing/boiling water (STP)
Thermistor extension from microcontroller module (10cm)
  Rigid fixture, allowing for ease of application to touch solid surface or penetrate fluid
  Thermistor protection from water damage
Both analog and digital signals must be used
User input for
  Sampling rate, error message if limit is exceeded
Digital temperature display in C and F
Error must stay within a certain tolerance (TBD)
User must be able to turn on/off the device
Notes: The overall objective of this project is to design a thermometer from an Arduino kit with an NTC thermistor. The requirements of this project are (go through points)

## Slide 8: Concept of Operations
Sampling Rate Specification
  User prompted input in Serial dialogue (Hz)
  Delay each loop by 1/input seconds
  Error message if invalid (more than limit)
  Limit determination
    Time one program loop : (millis command)
    Sampling rate limit : (conversion)
On/Off Buttons
  On button begins data collection, green LED on
  Off button terminates data collection, green LED off
Thermistor Placement
  User to press thermistor against solid or dip into fluid
  Need not to hold thermistor directly to avoid injury
Liquid Crystal Display (LCD)
  Potentiometer to vary contrast
  Celsius and Fahrenheit displayed
Steady State Indication/Criterion
  Blue LED
  Most recent 5(+) temperatures stored in array
  SS when all temps within 0.1 of another

## Slide 9: Operations/Tasks for Designer
Thermistor Calibration
  Voltage Divider to measure thermistor nominal resistance  choose second resistor
  Record thermistor resistance at three (freezing, room, boiling) known temps
    Use reference thermometer to record temps
  Three data points to calculate S-H constants (room temp for parameter)
Error Propagation and Uncertainty Analysis
  Factors in calculation of Temperature
    Thermistor Resistance
      Resistor 1 resistance
      Input Voltage
      Output Voltage
    S-H coefficients
      Three temperatures from reference thermometer
      Three thermistor resistances
  Different errors for C and F
Time Constant Measurement
  Take room temp reading
  Bring temp up to about 100C (boiling water)
  Remove thermistor from water, start timer
  Record time when temp = 63.2% diff
  Programmable
  Error Propagation

## Slide 10: Expected Results
Calibration
  Nominal Resistance
  T-R data
Time Constant
  Should be s (manufacturer specs)
Temperature error
  ideal (SS criterion)
  Expect something higher
Sampling Rate Limit
  Time to run one loop of program
  Possibly
  100,000 samples/sec
Point | Resistance () | Temperature ()
1 | 27101.45 | 3.1
2 | 11157.02 | 21.9
3 | 1390.16 | 83.2
Point |  | 
1 | 27101.45 | 3.1
2 | 11157.02 | 21.9
3 | 1390.16 | 83.2
Notes: Note c2 is small compared to others, beta parameter model assumption valid.

## Slide 11: System overview
Section 2

## Slide 12: Subsystem Definitions
Temperature Display
  How users will see/be able to read temperatures
On/Off buttons
  How users will turn display/program on and off
Voltage Divider
  How the thermistor is set up on the breadboard to determine its resistance
Thermistor Extension/Rigid Fixture
  How the thermistor will extend from module and its protection from environment
Steady State Criterion/Indicator
  How program will determine if steady state has been achieved and how users can determine if the temperature reading is stable and can be recorded
Arduino Code
  How the program is written to accomplish all objectives/requirements

## Slide 13: System Block Diagram
Microcontroller
Temperature Display (LCD)
On/Off Buttons
Thermistor Voltage Divider
Steady State Criterion
Arduino Program
Complete System
Potentio-
meter
Green LED
Blue LED
Rigid Extension & Protection
Notes: Go over color code: black: basic circuit components: pot, LED. Yellow: Subsystems of the design.
Go from left to right
Arduino program and microcontroller are sending information back and forth

## Slide 14: Critical Interfaces
Timing | System Component | Direction | Affects/Affected by
a | on/off buttons | input | begins/ends everything
a | Potentiometer | input | LCD
b | Green LED | output | on/off buttons
b | LCD | output | Potentiometer, on/off buttons
b | Thermistor | input//output | LCD, Blue LED // on/off buttons
c | Blue LED | output | on/off buttons, data collection rate
User must first input the sampling rate in serial monitor  defines delay in each loop
On/Off buttons: Send signals to start/end data collection
Potentiometer: Sends resistance information to affect contrast of LCD
Green LED: Turns on when system is running, i.e. on button has most recently been pressed. Turns off when system not running (off button)
LCD: Begins with blank screen. Contrast may be adjusted before on button. Once system is running, temperatures are displayed. When system is off, temperatures disappear, blank screen.
Thermistor: Sends information through voltage divider to program which converts VRT. Calculations and displays on LCD only made when system is ON
Blue LED: Can only work when system is ON. Turns on when SS reached, which is condition defined in program
Notes: I will walk through a sort of “typical” or “expected” cycle of temperature data collection using this chart and the descriptions below.

## Slide 15: System Setup
On Button
Off Button
Green LED
Blue LED
LCD
Potentiometer
Thermistor
Notes: On/Off buttons: Send signals to start/end data collection
Potentiometer: Sends resistance information to affect contrast of LCD
Green LED: Turns on when system is running, i.e. on button has most recently been pressed. Turns off when system not running (off button)
LCD: Begins with blank screen. Contrast may be adjusted before on button. Once system is running, temperatures are displayed. When system is off, temperatures disappear, blank screen.
Thermistor: Sends information through voltage divider to program which converts VRT. Calculations and displays on LCD only made when system is ON
Blue LED: Can only work when system is ON. Turns on when SS reached, which is condition defined in program

## Slide 16: Subsystem design
Section 3

## Slide 17: Temperature Display
Output temperature reading to LCD
Digital Signal
Given in Fahrenheit and Celsius
Requires “on” button
Variable contrast
Constant brightness
Risk:
  Using a potentiometer requires user to turn very small knob.
Mitigation:
  If this were to be a selling product, have versions with contrast already set with a resistor
TEMP: ___
TEMP: ___
POWER
Potentiometer
Resistor
CONTRAST
BRIGHTNESS
TEMP CALCULATION
TEXT
LCD
GROUND

## Slide 18: On/Off Buttons
On button
  Starts program and thermistor readings
  Turns green LED on
Off button
  Terminates program and thermistor readings
  Turns green LED off
  Clears LCD
Pressing button sends signal to microcontroller for limited time
Each loop checks which buttons send signal
Risk:
  Both buttons sending signals could cause problems
Mitigation:
  Create a condition to do nothing once one of the buttons turns off
POWER
GROUND
ON
OFF
Resistors
Buttons
DIGITAL SIGNAL PROCESSING
LED

## Slide 19: Thermistor Voltage Divider
Produces Output Voltage dependent on thermistor resistance
Arduino program to calculate thermistor resistance
Uses 10kOhm resistor in series with thermistor
5V input voltage
Analog signal
Risk:
  Using a resistor with resistance not close to nominal thermistor resistance may result in poor outputs/damage to thermistor
Mitigation:
  Use simple Voltage Divider to determine nominal resistance of thermistor first, then choose resistor accordingly before performing experiments at elevated/lowered temperatures
Resistor
THERMISTOR
POWER
GROUND
ANALOG SIGNAL PROCESSING

## Slide 20: Steady State Criterion
Program stores 5 most recent temperatures
Nested for loop to determine variance in values
If all values are within 0.1 Celsius, condition is met
Blue LED indicates SS
Risk:
  Sampling rate will change how often steady state is checked
Mitigation:
  Specify the sampling rate for steady-state check to be constant regardless of input.
LED
Resistor
DIGITAL SIGNAL PROCESSING
GROUND

## Slide 21: Rigid Extension/Protection
Extension
  Use Ribbon Wires to extend thermistor from breadboard
    Can use multiple connections to extend further distance
Protection
  Coffee stirring straws surrounding ribbon wires = rigidity
  Leave a bit of space before thermistor for rotational/dipping ability
  Nail polish to secure connections/extra layer of protection
  Electrical tape to surround wiring/connections
    Extra layer
Risk:
  Measuring extremely hot/cold bodies can be dangerous to user
Mitigation:
  Rigid extension allows user to hold bottom of wires far from sensor and still accurately position the thermistor

## Slide 22: Prototyping plan
Section 4

## Slide 23: Liquid Crystal Display
The LCD uses digital signal from microcontroller
Begin with basic setup and code
  Constant brightness/contrast using resistors
  Use basic commands in code to send messages to LCD
Shift to more variable interface
  Potentiometer to change contrast/brightness
Need to display calculated temperatures at specific locations on LCD

## Slide 24: LEDs
LED has two wires
Can be turned on/off when specific conditions are met
One end connects to resistor to ground
Other end connects to something to supply current
  Connect to voltage directly
  Connect to digital/analog signal
    When condition is met, signal is from microcontroller to LED, turns on
    Can also specify the LED to turn off with conditionals
ON/OFF LED
  Program conditionals to turn green LED on when ON button sends signal and OFF button is not sending signal
  Program conditionals to turn green LED off when ON button is not sending signal and OFF button sends signal
Steady-State LED
  Program a conditional to turn on blue LED when condition is met, turn off if not met

## Slide 25: Buttons
Buttons send a signal for limited time when pressed
Begin with experimenting with a single button to turn LED on
Program to ensure button stays on forever once button is pressed
Add another button to turn off LED when pressed.
Experiment with conditionals in code to find solution
Add LCD and data collection into loop
  Start data collection only if on button is pressed
  Stop data collection when off button is pressed
  Clear display when turned off
  Tell user to push on button to begin data collection

## Slide 26: Voltage Divider
Create a Voltage Divider with 2 constant resistors to find “unknown” resistance R2
Replace R2 with thermistor to determine nominal resistance
Replace R1 with appropriate resistor depending on nominal resistance
Add Voltage Divider with thermistor to entire circuit

## Slide 27: Project management
Section 5

## Slide 28: Schedule

## Slide 29: Budget
Costs
  Arduino Kit: $39.09
  Reference thermometer: $4.99
  Electrical tape: $9.99
  Straws: $4.99
  Total: $59.06

## Slide 30: Questions?